## Slide 1: The AQuA Converter An Analog Memory Cell
Micah O’Halloran
Prof. Rahul Sarpeshkar
Analog VLSI & Biological Systems Group
Jan. 25, 2002

## Slide 2: Uses of analog memory:
Circuit Offset Compensation
Self-Tuning/Adaptive Circuits
Learning Algorithms (Speech Processing, Robotics)
General Memory Element

## Slide 3: Two exisiting approaches to analog storage:
Floating-gate transistors
A/D/A converters

## Slide 4: Floating-Gate Transistors
A true analog voltage is stored on an SiO2 isolated floating gate using hot-electron injection and tunneling.
Notes: Pros:
Non-volatile
Can be compact
Cons:
Precise write requires iterative process ( 1 sec)
High voltage needed for erasing ( 25V)
Oxide degradation slows write time
Special process required
Precision of stored value degrades with time

## Slide 5: A/D/A – Analog-to-Digital-to-Analog Conversion
Notes: Pros:
Much faster storage than FGs
Stored precision does not degrade with time
Cons:
Digital conversion is wasteful of power/area
Parallel conversions require a lot of hardware

## Slide 6: Analog-to-Quantized-Analog (AQuA) Converter
No explicit digital conversion takes place
Uses clock as a quantizing tool

## Slide 7: AQuA Operation Overview
Step 1 – Sample Vin
Step 2 – Begin charging both caps
Step 3 – Csample asynchronously resets to zero when the voltage Vc1 reaches Vref1 . It then holds until the next positive clock edge.
Step 4 – Csample charges until Vo2 is high on a positive clock edge. Iclk is set so that Vo2 rises between the 2N-1 and the 2N clock edge (N is the number of bits we are quantizing to).
Step 5 – The conversion is complete once we reach a positive clock edge and Vo2 is high.
Notes: Basic operation is as follows:
1 bit’s worth of voltage is Isample multiplied by the clock period.
Sample the signal.
Charge the caps with Isample and Iclk, respectively.
When Vc1 hits Vref1, asynchronously reset Csample to zero volts and hold charging current until next positive clock edge.
Continue charging until Vo2 is high at a positive clock edge.
Shut all currents off when we have positive clock edge and Vo2 high.
Possible inquiries:
Q: Why not just use a counter? The scheme is then very similar to a single-slope converter idea.
A1: It is novel to be able to implement this idea without a digital counter because it still rounds to discrete attractors inherently.
A2: We project that the analog counter will be able to implement what we need – a count of 2^N clock ticks --for much less energy than a digital counter.
Q: How is Vref2 chosen?
A: It is chosen in conjunction with Iclk and the delay of the comparator on this cap to cause Vo2 to rise between the 2^N-1 and 2^N clock ticks. The absolute values of Iclk and
Vref2 can be very small in practical implementations to keep energy consumption in the circuit very low.
Q: How is Vref1 chosen?
A: This is defined to be the voltage that the cap Csample will be at after 2^N+0.5 clock ticks if the cap starts from zero. The algorithm depends on this being true for its
accuracy.
** Point out that the number of bits we can restore the signal to can by dynamically changed.
** Also point out that there is no need for matching of components in the circuit, because a tuning scheme will be use to take out inherent offsets on chip.

## Slide 8: Experimental Conversion

## Slide 9: AQuA Test Results – 6 bit

## Slide 10: Conclusion
The circuit was designed as a proof-of-concept of the AQuA idea, and achieved six bits of resolution.
The resolution of the implemented AQuA algorithm is very sensitive to the tuning of its parameters.
The design of a micropower 10-bit AQuA using a new more robust algorithm is currently underway.