## Slide 1: Metamaterials
Andrew Houck, Dave Kong,
Matt Reynolds, Peter Eckley,
J. Kong, Ike Chuang, Joe Jacobson

## Slide 2: Negative Index of Refraction
M.C.K. Wiltshire, Science 292: 60-61(2001)

## Slide 3: Potential Application: Focusing
Flat slab of metamaterial can act as a lens
Lack of axis allows lens to focus 2D and 3D images
M. Notomi, Phys Rev B 62, 10696 (2000)
J.B. Pendry, Phys Rev Lett 85, 3966 (2000)

## Slide 4: Manufacturing Negative 
Materials have negative permittivity slightly below the plasma frequency, which is typically in the visible spectrum in metals:
Periodic lattice of wires has reduced electron density, increased effective mass due to self induction  p ~ 10 GHz
J.B. Pendry et al, Phys. Rev. Let. 76, 4773 (1996)

## Slide 5: Manufacturing Negative 
Create magnetic resonance with nonmagnetic materials
Use split ring resonator to get capacitive-inductive resonance
Strong resonance gives negative 
J.B. Pendry et al, IEEE Trans. Microwave Theory Tech. 47, 2075 (1999).

## Slide 6: Metamaterial
Resonators and wires on opposite sides of printed circuit board (PCB)
Cut PCB into strips and assemble into a 2D lattice with 6 mm cell size
R.A. Shelby et al, Science 292, 77 (2001).

## Slide 7: Experimental Setup
Measure power spectrum as a function of angle
R.A. Shelby et al, Science 292, 77 (2001).

## Slide 8: Future Directions
Develop metamaterials that operate at different wavelengths
Use microwave metamaterial to verify interesting properties experimentally, such as focusing