## Slide 1: A MEMS Programmable Photonic Crystal?
Alexander D. Sprunt
Alexander H. Slocum, Advisor

## Slide 2: Photonic Crystal Possibilities
Light can be guided around sharp (less than ) corners by defects in photonic crystals in theory1 and in practice2 (1.55 m)
Only a few periods of the crystal are necessary for isolation, so it should be possible to create an optical switch with small programmable defects
1. J.D. Joannopoulos, R.D. Meade, J.N. Winn, Photonic Crystals (Princeton University Press, New York, 1995)
2. Lin S-Y, Chow E, Johnson SG, Joannopoulos JD, “Demonstration of highly efficient waveguiding in a photonic crystal slab at the 1.5-µm wavelength,” Optics Letters, vol. 25, no. 17, (2000)

## Slide 3: Results & Concepts
An appropriate defect, i.e. one that “pulls” a band into the bandgap of the bulk crystal, is created by shifting a line of cylinders horizontally.
The switch is actuated through a bi-stable mechanism, so power is only consumed at state changes
Field is confined to the defect region

## Slide 4: More Results and Concepts
Useful defects can also be created by adding material from out-of-plane
But this may lead to less elegant mechanisms
“plugs” added from outside the crystal

## Slide 5: Questions & Issues
A physicists perspective on the switch concept
Little experimental work has been done on “MEMS compatible” crystals and defects, why?