## Slide 1: Recent Research in Sensate Media
Joe Paradiso – Responsive Environments Group
MIT Media Lab
NSF/CBA 6/28

## Slide 2: Connecting to Your (Digital) Neighbors
Realization of “Paintable Computing” model (Butera)
Small computing nodes (25 MIPs) resembling thumb-tacks with two pins
Substrate provides power and ground
Talk to neighborhood via capacitive or IR coupling
Stacked architecture; header to provide each node with local sensor or actuator
First, coarse approach to a “skin” or sensate media
Testbed for very dense, dynamic sensor cluster and processor networks
Pushpin Computing
Josh Lifton

## Slide 3: Flexible Stacked Architecture

## Slide 4: Operating System Based on Paintable Principles

## Slide 5: Pushpin Status – Full system May 02
Pushpin on large conductive bulletin board
Courtesy of Steelcase
Pushpin w. IR comm layer

## Slide 6: Pushpins – June 02
Over 100 constructed
  Currently IR communication
All over MIT
  3 groups at Media Lab, AI Lab, Physics department
Sensor layer (photo sensor with LED outputs)

## Slide 7: Status and Applications
Software and hardware working
IR coupling is directional and anisotrophic
  Move to capacitive coupling with carrier (near-field RF)
Developing rules for distributed pattern recognition
  Project simple object (circle, square, triangle) onto array
Tangible interface for group dynamics (Steelcase)

## Slide 8: Intimate Digital Connection - Sensate Media
High-density local network of processors and sensors
Local computation finds features between adjacent nodes
  Communicates to outside world (edge…)
Sensors simple – could be capacitive, pressure, optical…
Pushes materials, interconnections, power distribution, network protocols…
Realization as smart surfaces, multisensory digital skins…
Revolutionary apps in medicine, wearables, robotics, HCI…

## Slide 9: Sensate Floors
Grid of piezoelectric wire
Massive multiplexer needed
Permanent exhibit at the MIT Museum (from 4/02)

## Slide 10: Z-Tiles (collaboration with U. Limerick, MLE)
Inspired by High Energy Physics e-calorimeters
Resistive silicon rubber “prexels” (1 cm x 1 cm)
Circa 16 prexels per tile
All tiles interlock, form peer-peer network
Tiles locally communicate to identify features
Parameters routed to edge connection