## Slide 1
Paintable Computing
Notes: The goal of the paintable computing project is to jointly develop millimeter scale computing elements and techniques for self-assembly of distributed processes.
The vision is a machine consisting of thousands of sand-grain sized processing nodes, each fitted with modest amounts of processing and memory, positioned randomly and communicating locally. Individually, the nodes are resource poor, vanishingly cheap and necessarily treated as freely expendable. Yet, when mixed together they cooperate to form a machine whose aggregate compute capacity grows with the addition of more node. This approach ultimately recasts computing as a particulate additive to ordinary materials such as building materials or paint.
The motivations for this work are low node complexity, ease of deployment, and tight coupling to dense sensor arrays, which all work to enable extraordinary scaling performance and to reduce the overall cost per unit compute capacity -- in some cases, dramatically.
The challenge is the explosive complexity at the system level; the cumulative effect of the unbounded node count, inherent asynchrony, variable topology, and poor unit reliability. In this regime, the limiting problem has consistently been the lack of a programming model capable of reliably directing the global behavior of such a system.
The strategy is to admit that we as human programmers will never be able to structure code for unrestricted use on this architecture, and to employ the principles of self-assembly to enable the code to structure itself.

## Slide 2
Paintable Computing
Die Cost
Notes: For IC’s sold en mass in a consumer market, the first order determinant of the price
is the size of the unpackaged die. Even immense one-time expenses for initial
development and plant (~ 109 $) can be amortized over monthly sales of several million units. In an industry characterized by a dizzying dynamic, the fixed cost of fabricating a single wafer (~ 102 $) has remained comparatively stable for decades. These fixed costs include manufacturing of the raw silicon ingot, slicing it into wafers, marching it through the ovens, packaging, and testing at multiple stages throughout the process. With the unit area of processed wafer as the fixed cost, the manufacturing cost for an individual IC depends on the percentage of the wafer’s dies that are functional — the yield. Alternatively, given a constant yield, the cost of a single IC depends the area of the die.
This simple relationship between yield, die size and unit cost have important consequences for economic viability of ultra-miniaturized computing nodes. A single defect is often enough to render an entire die inoperable. By drastically minimizing the economic penalty incurred by each defect, smaller dies enjoy a natural cost advantage over larger ones.
This log-log plot shows yield on a wafer as a function of defect count for three die sizes; 1 cm2 (large), 25 mm2 (medium), and 1 mm2 (small). Note that in the instance where 1060 failures leave one large die functional, the yield differential between the large and small dies approaches a factor of 200.

## Slide 3
Paintable Computing
Status
Hardware
Distributed Programming
Applications
Hardware Reference
Platform
Process Self-assembly
Storage,
Communications
Signal Processing
Notes: We've developed a reference platform for the computing nodes which admits a wide variety of designs and which IC manufactures regard as build-able -- in some cases, very simply.
We've developed a programming model based on "process self-assembly" – the unsupervised re-assembly of processes from autonomous fragments of code that are mobile in a virtual environment. This programming model has been embodied in a simulator that jointly serves as a pre-development tool for the hardware and a development environment for the software.
And we've demonstrated in simulation four representative applications that establish support for crucial functionalities: storage communication and signal processing.

## Slide 4
Paintable Computing
Process Self-assembly
Notes: The programming model is based on the novel concept of process self-assembly -- the unsupervised re-assembly of a running process from fragments of code which are mobile in a virtual environment.
Loosely following the analogy of reversible self-assembly in the material world, processes are broken up into fragments of code that are small, autonomous, and mobile. These process fragments (pfrags) enter the particle ensemble through randomly positioned I/O portals, migrate from particle to particle, and communicate with their immediately neighboring pfrags via posts to local bulletin boards.
Data exchanged between communicating pfrags enable them to emulate the physical forces of thermodynamic self-assembly as a guide to direct their spatial positioning. Pfrags also use this data exchange to decide whether to replicate, migrate further, erase themselves or simply do nothing.
The crucial point is that the computing substrate can be regarded as a fungible computational material that is not biased toward any particular task. And it is the interaction of propagating pfrags that leave this material configured for a particular task.
The movie shows pfrags cooperating to set up a point-to-point network. Each of the dot-sized icons is a device modeler in the simulator. Two groups of peers (larger circular icons) radiate broadcast messages in the form of propagating Gradient pfrags. These, in turn enable succeeding pfrags to construct a direct multi-channel link. Removal of one of the peers propagates a termination condition among the associated pfrags, ultimately returning the particle ensemble to its quiescent state.

## Slide 5
Paintable Computing
Original Applications
Media Streaming
Holistic Data Storage
Surface Bus
Image Segmentation
Notes: My dissertation (ftp://ftp.media.mit.edu/pub/bill/thesis/Final.Draft.pdf) describes four applications in detail:
In the first application – Streaming Media -- packetized media is streamed through a single port, randomizes its position for storage, and re-assembles itself into a serial order for output
Holistic Data Storage builds on this idea by adding signal processing to construct holistic representations for image storage – extending techniques for protection against transmission errors in noisy channels to the domain of faulty storage elements.
In Surface Bus, objects placed on the periphery of a 2D surface diffuse into the 2D ensemble small process fragments that replicate and self organize into a dynamic token ring.
And finally, Image Segmentation is realized as the competition among process fragments, each selective for image characteristics such as sky, water, trees, and sand
While these applications are currently running only in simulation, they already point to an important result. Namely that engineered functionality such as routing, signal processing and directed storage can be cast as an emergent behavior of interacting process fragments operating in a computationally homogeneous environment.

## Slide 6
Paintable Computing
On Deck
Hardware
Distributed Programming
Applications
Integration /
Prototype
Development
Environment
Audio / Image
Analysis
Notes: The remainder of this presentation roadmaps the ongoing work. While activity continues on all three fronts, my dissertation has brought a partial degree of closure to the programming model, and the focus has turned to the hardware and advanced applications.

## Slide 7
Paintable Computing
On Deck: Hardware
Pushpin I
Pushpin II
Single Package
Notes: Work on hardware will follow a relatively straight path of ever denser integration. The starting point is the pushpin computing work of Josh Lifton and Joe Paradiso(http://web.media.mit.edu/~lifton/Pushpin/). Here, computing nodes on the size scale of bottle caps draw power through pins from active planes in a layered composite, and communicate via IR.
The next revision of the hardware will adhere to this basic pushpin concept, extending the design to incorporate additional memory, a more powerful processor and extended support for debugging and code development.
The ultimate goal is a particle realized in a single monolithic IC (shown here as an artist conception).

## Slide 8
Paintable Computer
On Deck: Applications
Storage and Retrieval
Suburban Computing
Smart Materials
Parasitic
Super Computing
Notes: Ongoing work on applications, roughly divided into four classes, is discussed in the remaining seven slides.
The first application class deals with storage, query and retrieval. Initial results from the streaming media application experiment suggest that, within this important subset of computing, the paintable architecture may be resilient against the traditional scaling limitations of conventional symmetric multiprocessor designs.
The graph illustrates the typical scaling performance for parallel computing systems. This relationship, alternately referred to as Amdahl's law, states that the efficiency of parallel systems increases with the number of processors only up to a point. Beyond this point, the communication overhead associated with increasing the number of processors negatively impacts the efficiency. With further increases in processor count, the system performance ultimately arrives at a point where the addition of processors does not improve the overall performance.

## Slide 9
On Deck: Applications
Storage and Retrieval
Suburban Computing
Smart Materials
Parasitic
Super Computing
Paintable Computer
Notes: Extending the storage/retrieval techniques from the streaming media application, we are investigating query applications for which the paintable ensemble's performance scales monotonically with the number of particles.

## Slide 10
On Deck: Applications
Storage and Retrieval
Suburban Computing
Smart Materials
Parasitic
Super Computing
Paintable Computer
Notes: The second application class applies the basics of process self-assembly to length scales other than a paintable.
These next three slides consider the notion of suburban computing as an illustration of node sizes on the order of a PC card and inter-node spacing on the order of tens of meters. The device simulator for paintable computing is used as a first order test bed for applications targeted for use on a suburban scale.
This image shows an aerial photograph of a suburban neighborhood of single family homes in north Arlington, VA.

## Slide 11
On Deck: Applications
Storage and Retrieval
Suburban Computing
Smart Materials
Parasitic
Super Computing
Paintable Computer
Notes: The simulator models the case of a single node affixed to each home, and multiple nodes affixed to commercial and other non-residential structures (schools, roads, etc.).
In this image, the position of each house and small business has been retrieved manually and input into the simulator, which assigns a single "particle" to that location. Likewise, particles, are irregularly spaced along the roads and on the schools.

## Slide 12
On Deck: Applications
Storage and Retrieval
Suburban Computing
Smart Materials
Parasitic
Super Computing
Paintable Computer
Notes: This movie illustrates the instance of two parties in this network building pair-wise links for data transfer (e.g. a phone call).
While only a simulation, this movie hints the crucial point that homes, like paintable particles, can each be fitted with modest computational resources (e.g. a small card attached to the power meter) and seamlessly pool these resources into a super-computer-class aggregate. And that the functionality of this aggregate is can range from ad-hoc networking to concurrent solutions for sparse matricies.

## Slide 13
On Deck: Applications
Storage and Retrieval
Suburban Computing
Smart Materials
Parasitic
Super Computing
Paintable Computer
Notes: The third general class of applications is the domain of smart materials. In this regime, the computing elements are so finely granularized and so deeply embedded that the computational functionality of the material becomes almost indistinguishable from its basic material properties.
An example taken from my dissertation is the notion of Holistic Data Storage, where the collective memory of the particle ensemble is treated as a monolithic slab of memory, but with the unique characteristic that it stores images and sound holistically - arbitrary subsets of the memory yield reduced images of reduced resolution, in a manner reminiscent of a hologram.
In this illustration, an original image is sampled, encoded and stored in memory (shown as 2D planar surface). The original image can be reconstructed from the complete contents of the memory. However, when the memory element is damaged and only a small portion of the originally stored data is available (darkened portion of second storage surface), the reconstructed image is a low resolution copy of the original.

## Slide 14
On Deck: Applications
Storage and Retrieval
Suburban Computing
Smart Materials
Parasitic
Super Computing
104 particles / cinder block
103 cinder block
107 Hz. clock ticks / particle
1014 FLOPS
105 Watts
105 $
Paintable Computer
Notes: The fourth application class considers the impact of particles counts on the order of 107, where the particles are embedded into the foundations of small buildings. While this avenue of thinking is the least mature of the four, the economics of computing on this scale really beg the question of whether one can make sensible use of an ultra cheap supercomputer that is buried in the basement. And if so, what are the societal impacts?