## Slide 1: Dimensions in Silicon and in Biology
Simple molecules
<1nm
IBM PowerPC 750TM Microprocessor
7.56mm×8.799mm
6.35×106 transistors
semiconductor
nanocrystal (CdSe)
5nm
10-10
10-5
10-9
10-7
10-6
10-8
10-4
10-3
10-2
m
Circuit design
Copper wiring
width 0.2m
red blood cell
~5 m (SEM)
DNA
proteins
nm
bacteria
1 m
Nanometer memory element
(Lieber)
1012 bits/cm2 (1Tbit/cm2)
SOI transistor
width 0.12m
control biological machines
diatom
30 m
Notes: Engineering smaller and smaller machines
Self assembly: building things atom by atom. Issue: control! Esp. important if we are to build complex structures.
Biology has solved these problems: built extremely complex precise machines, which are small.
Why not take advantage of them and use them? Question of interface: can interface to inorganic world easily.
Goal: manipulate biological machines electronically.

## Slide 2: Biological machines
Compute (DNA)
  Input/Output
  Energetically efficient
  High data density
  Error correction
Self replication
Fabrication (synthesis) and breakdown
All processes highly efficient
How to take advantage of Nature’s engineering?

## Slide 3: Controlling Biology
Goals:
Control biological activity
  external
  reversible
  on molecular scale (selective)
  direct
  in vitro/ in vivo
  universal
M. Hoppert et al, American Scientist, 2001
Inside E.Coli
Notes: Control biological machines for assembly and computing
This is now a realistic goal due to advancements in xray crystallography and other structural characterization techniques. The field is at a point where one is able to understand on a very sophisticated level how some of these biomachines work: Have a molecular picture of how a ribosome or a polymerase works. Remarkable!
One important issue is how to interface to biology.

## Slide 4: Interfacing to biology
metal nanocrystal as antennas
  inductively heat the nanocrystal to heat biomolecule
  induce conformational change
Universality:
  Biomolecules denature with heat
  Structure: function correlation
RFMF
Au nanocrystal
“1”
“0”
active site
biomolecule
Notes: Control on simplest level: turn activity of something on and off. Switch between two states.
Certain characteristics we’d like this to have:
1.) Act on a molecular scale so that we can be selective. Crucial if we are faced with a whole ensemble of different molecules, we want to speak with a specific set of molecules and not everyone as a whole.
2.) addressing external, preferably electronic interface, so we determine when system is on and off and not the system
3.) applicable in vitro and in vivo: want the machines to be in their normal environment.
Approach: use inorganic nanocrystals and append them to biological system.
Through an alternating magnetic field, heat the nanocrystal. The nanocrystal transfers the heat to the protein, which slightly denatures. Through its change in conformation, the function is shut off.
Then, once the external field is turned off, the protein dissipates the heat and relaxes back to its normal structure and resumes activity.
Advantages to using nanocrystals:
Size (of proteins/DNA)
Soluble nanocrystals: two fold.
a)exchange of nanocrystals permits covalent linking to biology, chemistry already developed.
b)permits solubility of entire hybrid system. Crucial for invivo. This eliminates using a surface: biology does not like to be 2d! Effectively reducing the bio-inorganic interface to something very small and easy for the biology to handle.
Nanocrystals have been well studeied, and there are size and material dependent properties.

## Slide 5: Induction Heating
Alternating magnetic field induces alternating eddy currents in metal samples
For nm particles:
  f=1GHz (radiofrequency 109/s):
  Radiofrequency magnetic field: RFMF
Inductively heat solution
of gold nanocrystals
Ameritherm, Inc.
Induced current
in metal
Metal piece
alternating current i
frequency f
Magnetic field
Notes: How we speak to the nanocrystals: induction heating. Industrial technique used to heat macroscopic metal samples to high temperatures in a noncontact method.
Uses alternating magnetic field. Sample is placed in a coil, which has alternating current, makes alternating magnetic field. Alternating magnetic field induces eddy currents that switch direction back and forth at the frequency of the current. Generates heat. Picture: example of metal placed in an alternating magnetic field, gets hot where it’s inside the coil.
Now: use it to induce eddy currents inside the nanocrystals which are attached to the biological systems, everything in solution. Now only metal objects get heated.
Skin depth effect associated with induction heating: due to partial cancellation of the fields. In order to heat smaller objects, need to use higher frequencies.
Nm: GHz. Will call RFMF. Important to make clear that it is not an electromagnetic field but an magnetic field, changing direction 109X/s.
At first impression: may seem inappropriate: used for macroscopic materials, not precise. How will this result in something that behaves on the molecular scale and is selective? Turns out that due to size of the nanocrystals, the heat will be localized sufficiently to permit this.

## Slide 6: Controlled systems
DNA double stranded
DNA single stranded
Protein assembled:
active
Protein disassembled
into subunits: inactive
+
Molecular Machines group
Hamad-Schifferli, et al
Zhang group
Shi, et al
Notes: Three main ways we can switch on and off biological activity using a localized heat source.
Change structure, change function
Break up subunits of protein—many proteins out there that are composed of subunits, held together by noncovalent bonds (quarternary structure). Use induction heating of nanocrystal antenna to split these—yield protein inactive.
Use to dehybridize DNA.
Will describe nucleic acids: show its selective and specific, then describe enzyme of subunits.

## Slide 7: Biomolecular Machines
Manufacturing and assembly:
Polymerases, ligases, synthetases, ribosomes, ATP synthase, RNA ribozymes, telomerases,
Breakdown:
Proteases, nucleases, hydrolases, glycosidases, protesome, ATPases, ribozymes, DNAzymes.
Conversion:
Isomerases, dehydrogenases, protein kinases, phosphatases, transposases, oxidases, reductases, splicesome, chaperonin, transferases, deaminases.
Transport:
Hemoglobin, ion and amino acid transport proteins, nuclear receptors.
Signal transmission:
G-proteins, membrane ion channels, NMDA and other neurotransmitter receptors.
Structural Organization:
Histones/nucleosomes, collagens, keratins, actin, tubulin filaments, neurofilaments, dentin and other matrix proteins.
Binding receptors:
Antibodies, repressors, activators and other ion binding proteins.

## Slide 8: Control of expression: antisense
no protein
protein
antisense strand
(DNA 15-20mer)
ribosome
mRNA
AUG
DNA
RNA
protein
transcription
translation
polymerase
ribosome
RFMF
+
antisense strand
with Au
protein
protein
no protein
AUG
AUG

## Slide 9: Antisense in cells
1.) Transfection:
Electroporate
Chemically induced
peptide mediated
2.) RFMF
3.) detection: GFP (Green Fluorescent Protein)
RFMF
antisense
GFP
Protein expressed
Protein not expressed
Protein expressed