## Slide 1: BlueGene/L Supercomputer
George Chiu
IBM Research

## Slide 2
Notes: <number>
<footer>
<header>
<date/time>
Double in performance every 15 months

## Slide 3: BlueGene/L

## Slide 4: 512 Way BG/L Prototype

## Slide 5: BlueGene/L Interconnection Networks
3 Dimensional Torus
  Interconnects all compute nodes (65,536)
  Virtual cut-through hardware routing
  1.4Gb/s on all 12 node links (2.1 GB/s per node)
  Communications backbone for computations
  0.7/1.4 Tb/s bisection bandwidth, 67TB/s total bandwidth
Global Tree
  One-to-all broadcast functionality
  Reduction operations functionality
  2.8 Gb/s of bandwidth per link
  Latency of tree traversal 2.5 µs
  ~23TB/s total binary tree bandwidth (64k machine)
  Interconnects all compute and I/O nodes (1024)
Ethernet
  Incorporated into every node ASIC
  Active in the I/O nodes (1:64)
  All external comm. (file I/O, control, user interaction, etc.)
Notes: No one working on Infiniband's switch yet.
Torus bandwidth is 3 bytes/cycle (2bit x12/8)
Torus total BW 1.4Gb/sx6x64000 x1/8 = 67TB/s
Torus bisectional bandwidth 2(2 uni)x2(Torus)x32x64x1.4Gb/sx1byte/8bit = 1.4 TB/s
Torus latency is about 20 processor cycles
Global tree 16 levels deep
Global tree is 2bitx2 wiresx3portsx2directions/8=3bytes/cycle
Global tree total bandwidth 0.35GB/sx64K = 23 TB/s, where 2.8Gb/s /8 = 0.35GB/s
Static, deterministic routing
Each packet has a 256 byte payload, a 24 bit CRC
15ns per hub + capture/driver latency
16 classes/route/node
2 independent virtual networks
350 MOPS
Supports MPI_ALLREDUCE

## Slide 6: Complete BlueGene/L System at LLNL
BG/L
compute
nodes
65,536
BG/L
I/O nodes
1,024
Federated Gigabit Ethernet Switch
2,048 ports
Front-end nodes
Service node
WAN
visualization
archive
CWFS
8
8
Control network
8
512
128
64
48
1024

## Slide 7: Summary of performance results
DGEMM:
  92.3% of dual core peak on 1 node
  Observed performance at 500 MHz: 3.7 GFlops
  Projected performance at 700 MHz: 5.2 GFlops (tested in lab up to 650 MHz)
LINPACK:
  77% of peak on 1 node
  70% of peak on 512 nodes (1435 GFlops at 500 MHz)
sPPM, UMT2000:
  Single processor performance roughly on par with POWER3 at 375 MHz
  Tested on up to 128 nodes (also NAS Parallel Benchmarks)
FFT:
  Up to 508 MFlops on single processor at 444 MHz (TU Vienna)
  Pseudo-ops performance (5N log N) @ 700 MHz of 1300 Mflops (65% of peak)
STREAM – impressive results even at 444 MHz:
  Tuned: Copy: 2.4 GB/s, Scale: 2.1 GB/s, Add: 1.8 GB/s, Triad: 1.9 GB/s
  Standard: Copy: 1.2 GB/s, Scale: 1.1 GB/s, Add: 1.2 GB/s, Triad: 1.2 GB/s
  At 700 MHz: Would beat STREAM numbers for most high end microprocessors
MPI:
  Latency – < 4000 cycles (5.5 s at 700 MHz)
  Bandwidth – full link bandwidth demonstrated on up to 6 links

## Slide 8
Applications
BG/L is a general purpose technical supercomputer
N-body simulation
  molecular dynamics (classical and quantum)
  plasma physics
  stellar dynamics for star clusters, galaxies
Complex multiphysics code
  Computational Fluid Dynamics (weather, climate, sPPM...)
  Accretion
  Raleigh-Jeans instability
  planetary formation and evolution
  radiative transport
  Magnetohydrodynamics
Modeling thermonuclear events in/on astrophysical objects
  neutron stars
  white dwarfs
  supernovae
Radiotelescope
FFT
Notes: <number>
<footer>
<header>
<date/time>
BOB: Built on Beowulf, Tom Sterling's machine.

## Slide 9
  Summary
    Embedded technology promises to be an efficient path toward building massively parallel computers optimized at the system level.
    Cost/performance is ~20x better than standard methods to get to TFlops.
    Low Power is critical to achieving a dense, simple, inexpensive packaging solution.
    Blue Gene/L will have a scientific reach far beyond existing limits for a large class of important scientific problems.
    Blue Gene/L will give insight into possible future product directions.
    Blue Gene/L hardware will be quite flexible. A mature, sophisticated software environment needs to be developed to really determine the reach (both scientific and commercial) of this architecture.