## Slide 1
Three Dimensional Integrated Circuits
C.S. Tan, A. Fan, K.N. Chen, S. Das, N. Checka and R. Reif
Microsystems Technology Laboratories
M.I.T.

## Slide 2
3-D Integrated Circuits (3-D IC)
A vertical stack of multiple device and interconnect layers connected together by interlayer vertical vias.
Device/Interconnect Layer
Interlayer Vertical Via

## Slide 3
3-D IC with Cu-Cu Wafer Bonding
(R. Reif, MIT)
Interlayer Vertical Via
Cu-Cu Bonding
M3
M2
M1
M3
M2
M1
M4
DL2
DL1
DL – Device Layer
M – Metal Interconnect Layer

## Slide 4
How Does 3-D Integration Help?
Greater number of nearest neighbors for a given transistor
Every transistor, gate, and module has increased wiring bandwidth
Interconnect distribution becomes shifted
  Fewer global wires, more local wires
Energy consumption and cycle time reduced
More effective use of Si area
Wire-length
Number of Interconnects
(Log-Log Plot)
2-D IC
3-D IC

## Slide 5
Digital Block Partitioning
2D
3D
  Exploit locality to reduce interconnect lengths
  Reduce chip area for interconnect-dominated applications
  Increase density for device-dominated applications

## Slide 6
Mixed-Signal Partitioning
2D
3D
  Mixed-technology/mixed-signal based applications
  Better signal isolation between analog and digital components

## Slide 7
Monolithic integration of different dies
3D
2D
Smaller form factor
-Reduced power dissipation and/or energy consumption

## Slide 8
3-D Approaches
Parallel fabrication, layer transfer by bonding
- Dielectric : polymer, SiO2
- Metallic : Cu-Cu
Continuous layer growth/fabrication

## Slide 9
Cu-Cu Wafer Bonding
(R. Reif, MIT)
Interlayer Vertical Via
Cu-Cu Bonding
M3
M2
M1
M3
M2
M1
M4
DL2
DL1
DL – Device Layer
M – Metal Interconnect Layer

## Slide 10
Crystallization of -Si
Bulk Si
n+/p+
n+/p+
n+/p+
Gate
Gate
T1
T2
M1
M2
M3
M4
n+/p+
n+/p+
Gate
n+/p+
M’1
M’2
VILIC
Via
Memory or
Analog
Recrystallized Si
Logic
Repeaters or
optical I/O devices
(K.Saraswat, Stanford)

## Slide 11
3-D Research @ MIT
Process Technology Development
CAD Tool Development
Applications: 3-D Circuit/System
- Partitioning Digital Circuits
- Partitioning Mixed-Signal Circuits
- Monolithically integrating several dies

## Slide 12
Process Technology Development

## Slide 13
BOX
M1 (Al)
M1 (Al)
LOCOS/STI
LOCOS/STI
Cu Via
Cu Pad
Parallel FEOL Processes on 2 Device Wafers
Device/Interconnect Layer 2 (SOI)
Device/Interconnect Layer 1 (Bulk Si)

## Slide 14
Handle wafer provides mechanical support and ease of wafer handling
Strong enough to withstand subsequent process
Ease of release
SOI Wafer is attached to a handle wafer
SOI Wafer Thinning
SOI wafer etch back
A combination of mechanical grinding, plasma dry etch and chemical wet etch
Advantage of SOI – Etch stop on BOX
Cu Via and Pad formation
Via etch, passivation, barrier layer and fill
Cu Pad for bonding
Precision alignment and bonding

## Slide 15
Optical alignment
Back-to-face bonding
Cu to Cu Bonding
Via pad is for electrical connection
Dummy pad is to increase bonding strength
Precision alignment and bonding
Handle Wafer Release
Fast process is required to minimize damage to the stack

## Slide 16
Cu Contact Bonding
10 µm contact
10 um contact
SEM image
TEM image
SEM image
SEM image
(K.N.Chen)

## Slide 17
CAD Tool Development

## Slide 18
FFT – Energy Consumption
27% - 40% reduction in switching energy
Can obtain almost all the energy savings while maintaining cycle time

## Slide 19: Future
Introduce nanotubes/nanowires
  Develop active/passive interconnects (wires that process and/or transmit information)
  Develop insulators with high thermal conductivities (thermal profiles)
  Develop nano-inductors (RF applications)