## Slide 1: Improving FLOPS/Watt by Computing Reversibly, Adiabatically, & Ballistically
Presented at the Workshop on Energy and Computation: Flops/Watt and Watts/Flop, Center for Bits and Atoms, MIT Wednesday, May 10, 2006
(CRAB-ing?)

## Slide 2: Reversible Computing and Adiabatic Circuits
or How to open the door towards ever-improving computational energy efficiency
and (just maybe) save civilization from eventual technological stagnation!

## Slide 3: Outline of Talk
Outline:
  Motivation
  Principles
  Technology
  The Future
More detailed list of topics:
  Everyone has it all wrong!
  Energy Efficiency
  VNL Principle
  Reversible Logic
  Adiabatic Principle
  Almost-Perpetual Motion?
  Adiabatic Rules
  Example Results
  Scaling Laws
  Device Requirements
  Breakthroughs Needed
  Help Save the Universe!

## Slide 4: Efficiency in General, and Energy Efficiency
The efficiency η of any process is: η = P/C
  Where P = Amount of some valued product produced
  and C = Amount of some costly resources consumed
In energy efficiency ηe, the cost C measures energy.
We can talk about the energy efficiency of:
  A heat engine: ηhe = W/Q, where:
    W = work energy output, Q = heat energy input
  An energy recovering process : ηer = Eend/Estart, where:
    Eend = available energy at end of process,
    Estart = energy input at start of process
  A computer: ηec = Nops/Econs, where:
    Nops = # useful operations performed
    Econs = free-energy consumed

## Slide 5: Trend of Min. Transistor Switching Energy
Practical limit for CMOS?
Naïve linear extrapolation
fJ
aJ
zJ
Based on ITRS ’97-03 roadmaps
Node numbers (nm DRAM hp)
CV2/2 gate energy, Joules

## Slide 6: Everyone Has It All Wrong!
As the talk proceeds,
  I’ll explain (in the proud MIT tradition) why most of the rest of the world is thinking about the future of computing in a completely wrong-headed way.
In particular,
  The Low-Power Logic Circuit Designers have it all wrong!
  The Semiconductor Process Engineers have it all wrong!
  (Most) Device Physicists have it all wrong!

## Slide 7: The von Neumann-Landauer (VNL) principle
John von Neumann, 1949:
  Claim: The minimum energy dissipated “per elementary (binary) act of information” is kT ln 2.
    No published proof exists; only a 2nd-hand account of a lecture
Rolf Landauer (IBM), 1961:
  Logically irreversible (many-to-one) bit operations must dissipate at least kT ln 2 energy.
    Paper anticipated but didn’t fully appreciate reversible computing
One proper (i.e. correct) statement of the principle:
  The oblivious erasure of a known logical bit generates at least k ln 2 amount of new entropy.
    Releasing into environment at T requires kT ln 2 heat emission.

## Slide 8: Proof of the VNL Principle
The principle is occasionally questioned, but:
  Its truth follows absolutely rigorously (and even trivially!) from rock-solid principles of fundamental physics!
(Micro-)reversibility of fundamental physics implies:
  Information (at the microscale) is conserved
    I.e., physical information cannot be created or destroyed
      only transformed via reversible, deterministic processes
  Thus, when a known bit is erased (lost, forgotten) it must really still be preserved somewhere in the microstate!
    But, since its value has become unknown, it has become entropy
      Entropy is just unknown/incompressible information

## Slide 9: Types of Dynamical Processes
These animations illustrate how states transform in their configuration space, in:
  A nondeterministic process:
    One-to-many transformations
  An irreversible process:
    Many-to-one transformations
  Nondeterministic and irreversible:
  Deterministic and reversible:
    One-to-one transformations only!
WE ARE HERE

## Slide 10: Physics is Reversible!
Despite all of the empirical phenomenology relating to macro-scale irreversibility, chaos, and nondeterministic quantum events,
  Our most fundamental and thoroughly-tested modern models of physics (e.g. the Standard Model) are, at bottom, deterministic & reversible!
    All of the observed nondeterministic and irreversible phenomena can still be explained within such models, as emergent effects.
  Although classical General Relativity is argued by some researchers to have certain irreversible aspects,
    The general consensus seems to be that we’ll eventually find that the “correct” theory of quantum gravity will be reversible.

## Slide 11: Reversible/Deterministic Physics is Consistent with Observations
Apparent quantum nondeterminism can validly be understood as an emergent phenomenon, an expected practical result of permanent wavefunction splitting
  As illustrated e.g. in the “many worlds” and “decoherent histories” pictures
Even if a quantum wavefunction does not split permanently, its evolution in a large system can quickly become much too complex to track within our models
  Thus we resort to using “reduced” density matrices, which discard some knowledge
The above effects, plus imprecision in our knowledge of fundamental constants, result in some practical unpredictability even for microscale systems
  Thus entropy, for all practical purposes, tends to increase towards its maximum
Chaos (macro-scale nondeterminism) occurs when entropy at the microscale infects our ability to forecast the long-term evolution of macroscopic variables
  A necessary consequence of the computation-universality of physics?
Meanwhile, averaging of many high-entropy microscopic details results in a “smoothing” effect that leads to irreversible evolution of macro-variables.

## Slide 12: Reversible Computing
We’d like to design mechanisms that compute while producing as little entropy as possible…
  In order to minimize consumption of free energy / emission of heat to the environment
Losing known information necessarily results in a minimum k ln 2 entropy increase per bit lost, so…
  Let’s consider what we can do using logically reversible (one-to-one) operations that don’t lose information.
Such operations are still computationally universal!
  Lecerf (1963), Bennett (1973)

## Slide 13: Conventional Gate Operations are Irreversible (even NOT!)
time
Consider a computer engineer’s (i.e., real world!) Boolean NOT gate (a.k.a. logical inverter)
  Specified function: Destructively overwrite output node’s value with the logical complement of the input!
in
out
Old in
Old out
Hardware diagram:
Space-time logic network diagram (not the same thing!!):
New
in
New
out
Two different physical logic nodes
Inverter gate
Inverter operation

## Slide 14: In-Place NOT (Reversible)
Computer scientist’s (i.e., somewhat fictionalized!) in-place logical NOT operation
  Specified operation: Replace a given logic signal with its logical complement.
    People occasionally confuse the irreversible inverter operation with a reversible in-place NOT operation
      The same icon is sometimes used in spacetime diagrams
in
out
old bit
new bit
time
time

## Slide 15: In-Place Controlled-NOT (cNOT)
Specified function: Perform an in-place NOT on the 2nd bit if and only if the 1st bit is a 1.
  Equiv., replace 2nd bit with XOR of 1st & 2nd bits
control
old
data
new
data
Before |  | After | 
C | D | C | D
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Transition table
time

## Slide 16: Early Universal Reversible Gates
Controlled-controlled-NOT (ccNOT)
  A.k.a. Toffoli gate
    Perform cNOT(b,c) iff a=1.
    Equiv., c := c XOR (a AND b)
Controlled-SWAP (cSWAP)
  A.k.a. Fredkin gate
    Swap b with c iff a=1.
  Conserves 1s
A
B
C
A
B
C

## Slide 17: The Adiabatic Principle
Applied physicists know that a wide class of physical transformations can be done adiabatically
  From Greek adiabatos, “It shall not be passed through”
    I.e., no passage of heat through an interface separating subsystems at different temperatures
  Newer, more general meaning: No increase of entropy
    Of course, exactly zero entropy increase isn’t practically doable
In practice, “adiabatic” is used to mean that the entropy generation scales down proportionally as the process takes place more gradually.
  The general validity of this 1/t scaling relation is enshrined in the famous adiabatic theorem of quantum mechanics.

## Slide 18: Adiabatic Charge Transfer
Consider passing a total quantity of charge Q through a resistive element of resistance R over time t via a constant current, I = Q/t.
  The power dissipation (rate of energy diss.) during such a process is P = IV, where V = IR is the voltage drop across the resistor.
The total energy dissipated over time t is therefore: E = Pt = IVt = I2Rt = (Q/t)2Rt = Q2R/t.
  Note the inverse scaling with the time t.
In adiabatic logic circuits, the resistive element is a switch.
  The switch state can be changed by other adiabatic charge transfers.
  In simple FET-type switches, the constant factor (“energy coefficient”) Q2R appears to be subject to some fundamental quantum lower bounds.
    However, these are still rather far away from being reached.
R
Q

## Slide 19: Reversible and/or Adiabatic VLSI Chips Designed @ MIT, 1996-1999
By EECS Grad Students Josie Ammer, Mike Frank, Nicole Love, Scott Rixner, and Carlin Vieri under CS/AI lab members Tom Knight and Norm Margolus.
Notes: So anyway, using another (more complicated, and buggy) adiabatic logic style, my collaborators and I built these reversible chips at MIT (under Tom Knight and Norm Margolus) to demonstrate that the architectural problems of reversible logic are straightforward to solve. Tick (by myself and Scott Rixner) was a simple non-adiabatic microprocessor implemented in standard CMOS that nevertheless implemented a logically reversible machine-language instruction set, as a proof-of-concept and basis for comparison with fully-adiabatic circuits. FlatTop (me, Nicole Love, Carlin Vieri, Josie Ammer) was the first scalable, universal, fully-adiabatic reconfigurable processor, capable of efficiently simulating 2D and 3D reversible circuits of arbitrary complexity when tiled in large arrays. (FlatTop works by simulating in SCRL the Margolus BBMCA cellular automaton which itself simulates Fredkin’s BBM billiard ball model of reversible computing which itself simulates reversible logic networks composed of Fredkin gates, which themselves can simulate arbitrary reversible CAs – the simulation is so indirect that it is not very efficient, but it is universal for reversible CAs with “only” constant-factor overhead. Anyway it is just a proof of concept.) XRAM (Carlin, Josie) was an adiabatic memory with a reversible interface (though I have since invented far more efficient ones), and Pendulum (Vieri, with ISA mods from me) was a complete, fully-adiabatic, MIPS-style microprocessor.
This chip-design work (the Pendulum project, DARPA-funded under the Scalable Computing Systems Program) demonstrated that reversible logic is by no means incompatible with traditional styles of computer organization. It only requires a fairly minor translation of traditional architectural methods.
However, this work begged the question: Can reversible computing ever really be cost-effective? Can the overheads of reversible and adiabatic operation ever be outweighed by their energy savings?
It was the goal of my subsequent research to answer this question, using a principled systems-engineering methodology which I will describe.

## Slide 20: The Low-Power Design community has it all wrong!
Even (most of) the ones who know about adiabatics and even many who have done extensive amounts of research on adiabatic circuits still aren’t doing it right!
  Watch out! 99% of the so-called “adiabatic” circuit designs published in the low-power design literature aren’t truly adiabatic, for one reason or another!
As a result, most published results (and even review articles!) dramatically understate the energy efficiency gains that can actually be achieved with correct adiabatic design.
  Which has resulted in (IMHO) too little serious attention having been paid to adiabatic techniques.

## Slide 21: Circuit Rules for True Adiabatic Switching
Avoid passing current through diodes!
  Crossing the “diode drop” leads to irreducible dissipation.
Follow a “dry switching” discipline (in the relay lingo):
  Never turn on a transistor when VDS ≠ 0.
  Never turn off a transistor when IDS ≠ 0.
Together these rules imply:
  The logic design must be logically reversible
    There is no way to erase information under these rules!
  Transitions must be driven by a quasi-trapezoidal waveform
    It must be generated resonantly, with high Q
Of course, leakage power must also be kept manageable.
  Because of this, the optimal design point will not necessarily use the smallest devices that can ever be manufactured!
    Since the smallest devices may have insoluble problems with leakage.
Important but often neglected!
Notes: Now, in order for a logic circuit to be truly adiabatic, you have to follow certain rules. First, never pass current through diodes, so, you have to avoid bipolar transistors, for example – field-effect transistors only! Next, you have to follow a “dry switching” discipline as the old relay electronics people used to call it. To prevent sparking and corrosion on contacts, you never turn on a switch when there is a voltage across it, and never turn it off when there is a current through it. Many of the so-called “adiabatic” circuits you find in the literature actually break the second rule and so are not truly adiabatic. Anyway, together these rules imply that the logic design has to be reversible (since there is no way to erase information under these constraints), and it also turns out you need a voltage waveform that has flat tops and bottoms (is quasi-trapezoidal) because otherwise you’ll never be able to turn off a transistor since there will always be a current through it (except for infinitesimal moments). Finally, the voltage waveform needs to be generated resonantly, with high Q. Leakage power consumed by nominally turned-off transistors also needs to be kept low, and I believe that because of this the scaling of devices will soon halt. The optimal devices will not necessarily be the smallest ones we can manufactured, since these have high leakage rates.

## Slide 22: Conditionally Reversible Gates
Avoiding VNL actually only requires that the operation be one-to-one on the subset of states actually encountered in a given system
  This allows us to design with gates that do conditionally reversible operations
    That is, they are reversible if certain preconditions are met
    Such gates can be built easily using ordinary switches!
  Example: cSET (controlled-SET) and cCLR (controlled-CLR) operations can be implemented with a single digital switch (e.g. a CMOS transmission gate), with operation & timing controlled by an externally-supplied driving signal
    These operations are conditionally reversible, if preconditions are met
drive
out
in
01
10
old out = 0
in
new out = in
final out = 0
Hardware schematic:
Space-time logic diagram
Hardware icon:
in
out
drive

## Slide 23: Reversible OR (rOR) from cSET
Semantics: rOR(a,b)::=if a|b, c:=1.
  Set c:=1, if either a or b is 1.
    Reversible if initially a|b → ~c.
Two parallel cSETs simultaneously driving a shared output bus implements the rOR operation!
  This is a type of gate composition that was not traditionally considered.
Similarly, one can do rAND, and reversible versions of all Boolean operations.
  Logic synthesis with these is extremely straightforward…
c
b
a
a’
b’
c’
0
a OR b
a
b
c
Spacetime diagram
Hardware diagram

## Slide 24: Simulation Results (Cadence/Spectre)
Graph shows power dissipation vs. frequency
  in 8-stage shift register.
At moderate frequencies (1 MHz),
  Reversible uses < 1/100th the power of irreversible!
At ultra-low power (1 pW/transistor)
  Reversible is 100× faster than irreversible!
Minimum energy dissip. per nFET is < 1 eV!
  500× lower than best irreversible!
    500× higher computational energy efficiency!
Energy transferred is still ~10 fJ (~100 keV)
  So, energy recovery efficiency is 99.999%!
    Not including losses in power supply, though
1 nJ
100 pJ
10 pJ
1 pJ
100 fJ
10 fJ
1 fJ
100 aJ
10 aJ
1 aJ
100 zJ
10 zJ
1 zJ
kT ln 2
1 eV
Standard CMOS
2V
1V
0.5V
0.25V
2LAL 1.8-2V
Energy dissipated per nFET per cycle
100 yJ
2LAL = Two-level adiabatic logic (invented at UF, ‘00)

## Slide 25: Semiconductor Process Engineers have it all wrong!
Everybody still thinks that smaller FETs operating at lower voltages will forever be the way to obtain ever more energy-efficient and more cost-efficient designs.
  But if correct adiabatic design techniques are included in our toolbox, this is simply not true!
    With good energy recovery, higher switching voltages (requiring somewhat larger devices) enable strictly greater overall energy efficiency! (and thus lower energy cost!)
      This is due to the suppression of FET leakage currents exponentially with Vq/kT.
    The hardware cost-performance overheads of this approach only grow polylogarithmically with the energy efficiency gains
      Over time, we can expect the overheads will be overtaken by competitively-driven per-device manufacturing cost reductions
  If devices better than FETs aren’t found,
    then I predict an eventual “bounce” in device sizes

## Slide 26: The Need for Ballistic Processes
In order to achieve low overall entropy generation in a complete system,
  Not only must the logic transitions themselves take place in an adiabatic fashion,
    but also the components that drive and control the signal levels and timing of logic transitions (“power clocks”) must proceed reversibly along the desired trajectory.
Thus, we require a ballistic driving mechanism:
  One that proceeds “under its own momentum” along a desired trajectory with relatively little entropy increase.
    Many concepts for such mechanisms have been proposed, but…
      Designing a sufficiently high-quality power-clock mechanism remains the major unsolved problem of reversible computing

## Slide 27: Fredkin and Toffoli’s (1980) Billiard-Ball Model of Computation
1st conceptual model of a ballistic physical computing process
  Perfectly rigid “billiard balls” bounce off walls & each other in digitally-precise trajectories
  Shown to be capable of asymptotically efficient simulations of arbitrary reversible circuits in 2D (extensible to 3D also)
It’s idealized; it would be chaotically unstable in practice
  The addition of appropriate constraining mechanisms to prevent the balls from going “off track” or “out of sync” is viewed as a later step
  Zurek argued that analogous quantum processes can avoid the chaos

## Slide 28: Requirements for Energy-Recovering Clock/Power Supplies
All of the known reversible computing schemes require the presence of a periodic and globally distributed signal that synchronizes and drives adiabatic transitions in the logic.
  For good system-level energy efficiency, this signal must oscillate resonantly and near-ballistically, with a high effective quality factor.
Several factors make the design of a resonant clock distributor that has satisfactorily high efficiency quite difficult:
  Any uncompensated back-action of logic on resonator
  In some resonators, Q factor may scale unfavorably with size
  Excess stored energy in resonator may hurt the effective quality factor
There’s no reason to think that it’s impossible to do it…
  But it is definitely a nontrivial hurdle, that we reversible computing researchers need to face up to, pretty urgently…
    If we hope to make reversible computing practical in time to avoid an extended period of stagnation in computer performance growth.

## Slide 29: MEMS Resonator Concept
Moving
plate
Moving metal plate support arm/electrode
Range of Motion
Arm anchored to nodal points of fixed-fixed beam flexures, located a little ways away, in both directions (for symmetry)
Phase 0° electrode
Phase 180° electrode
θ
0°
360°
C(θ)
C(θ)
θ
0°
360°
…
Repeat interdigitated structure arbitrarily many times along y axis, all anchored to the same flexure
x
y
z
(PATENT PENDING, UNIVERSITY OF FLORIDA)

## Slide 30: MEMS Quasi-Trapezoidal Resonator: 1st Fabbed Prototype
Post-etch process is still being fine-tuned.
  Parts are not yet ready for testing…
(PATENT PENDING, UNIVERSITY OF FLORIDA)
Drive comb
Sense comb
Primary flexure (fin)
(Funding source: SRC CSR program)

## Slide 31: Would a Ballistic Computer be a Perpetual Motion Machine?
Short answer: No, not quite!
  Hey, give us some credit here!
    We’re hard-core thermodynamics geeks, we know better than that!
Two traditional (and impossible!) kinds of perpetual motion machines:
  1st kind: Increases total energy - Violates 1st law of thermo. (energy conservation)
  2nd kind: Reduces total entropy - Violates 2nd law of thermo. (entropy non-decrease)
Another kind that might be “possible” in an ideal world, but not in practice:
  3rd kind: Produces exactly 0 increase in entropy!
    Requires perfect knowledge of physical constants, perfect isolation of system from environment, complete tracking of system’s global wavefunction, no decoherence, etc.
What we’re more realistically trying to build in reversible computing is none of the above, but only the more modest goal of a “For-a-long-time Motion Machine”
  I.e., one that just produces as close to zero entropy (per op) as we can possibly achieve!
    It would “coast” along for a while, but without energy input, it would eventually halt
  Such a “coasting” machine can perform no net mechanical work in a complete cycle,
    But it can potentially do a substantial amount of useful computational work!

## Slide 32: Some Results on Scalability of Reversible Computers
In a realistic physics-based model of computation that accounts for thermodynamic issues:
  When leakage is negligible and heat flux density is bounded,
    Adiabatic machines asymptotically outperform irreversible machines (even per unit cost!) as problem sizes & machine sizes are scaled up
      But, the absolute speedup when total system power is unrestricted grows only as a small polynomial with the machine size
        E.g., exponents of 1/36 or 1/18, depending on problem class
      The speedup per unit surface area or (equivalently) per unit power dissipation grows at a somewhat faster (but still gradual) rate
        E.g., with the 1/6 power of machine size
  Even when leakage is non-negligible,
    Adiabatic machines can still attain constant-factor (i.e., problem-size-independent) energy savings (& speedups at fixed power) that scale as moderate polynomials of the device characteristics
      E.g., roughly with the transistor on-off ratio to at least the ~0.39 power
    Cost overheads from RC in these scenarios also grow, somewhat faster
      But, we can hope that device costs will continue to decline over time

## Slide 33: Bennett’s 1989 Algorithm for Worst-Case “Reversiblization”
k = 2 n = 3
k = 3 n = 2

## Slide 34: Worst-Case Energy/Cost Tradeoff (Optimized Bennett-89 Variant)
Spacetime cost blowup factor
Energy savings factor
k
n
cost  energy 1.59

## Slide 35: Device Physicists have it all wrong!
Unfortunately, I’d say >90% of papers published on new logic device concepts (whether based on CNTs, spintronics, etc.) either ignore or dramatically neglect the key issue of the energy efficiency of logic operations
  Even though, looking forward, this is absolutely the most crucial parameter limiting the practical performance of leading-edge computing systems!
    And, even the rare few device physicists who study reversible devices don’t seem to be talking to the analog/RF/µwave engineers who might help them solve the many subtle and difficult problems involved in building extremely high-quality energy-recovering power-clock resonators

## Slide 36: Device-Level Requirements for Reversible Computing
A good reversible digital bit-device technology should have:
  Low amortized manufacturing cost per device, ¢d
    Important for good overall (system-level) cost-efficiency
  Low per-device level of static “standby” power dissipation Psb due to energy leakage, thermally-induced errors, etc.
    This is required for energy-efficient storage devices, especially
      but it’s still a requirement (to a lesser extent) in logic as well
  Low energy coefficient cEt = Ediss·ttr (energy dissipated per operation, times transition time) for adiabatic transitions between digital states.
    This is required in order to maintain a high operating frequency simultaneously with a high level of computational energy efficiency.
      And thus maintain good hardware efficiency (thus good cost-performance)
  High maximum available transition frequency fmax.
    This is especially important for applications in which the latency from inherently serial computing threads dominates total operating costs

## Slide 37: Plenty of Room for Device Improvement
Recall, irreversible device technology has at most ~3-4 orders of magnitude of power-performance improvements remaining.
  And then, the firm kT ln 2 (VNL) limit is encountered.
But, a wide variety of proposed reversible device technologies have been analyzed by physicists.
  With preliminary estimates of theoretical power-performance up to 10-12 orders of magnitude better than today’s CMOS!
    Ultimate limits are unclear.
.18µm CMOS
.18µm 2LAL
k(300 K) ln 2
Various reversible device proposals
Power per device, vs. frequency

## Slide 38: One Optimistic Scenario
Note that by 2020, there could be a factor of 20,000× difference in raw performance per 100W package. (E.g., a 100× overhead factor from reversible design could be absorbed while still showing a 200× boost in performance!)
40 layers, ea. w. 8 billion active devices, freq. 180 GHz, 0.4 kT dissip. per device-op
e.g. 1 billion devices actively switching at 3.3 GHz, ~7,000 kT dissip. per device-op

## Slide 39: How Reversible Computing Might (Someday) Save the Universe
In case the potential practical benefits in the next few decades aren’t enough motivation for us to study reversible computing, consider the following:
  The total free energy resources (related to bits of “extropy”) that we can access are ultimately finite
    Thus, any civilization based on irreversible ops necessarily has a finite lifetime!
      Holographic bound suggests universe has only ~10120 or so bits of extropy
  But, a civilization based on an exponentially-improving reversible computing technology could (potentially) do infinitely many ops using only finite free energy!
    Eventually, you will still hit the Poincare recurrence time within the horizon, and run out of new distinguishable quantum states to explore,
      but before this happens, you could still perform exponentially more ops than any irreversible civilization could ever possibly do!
  I.e. reversible computing could potentially someday “save the universe” from a premature heat death…

## Slide 40: finis

## Slide 41: Finiteness of Our Causally Connected Universe
Astronomical observations indicate the expansion of the universe is accelerating!
  As if by a small positive cosmological constant
    A kind of repulsive energy density uniformly filling all space
Observed value would imply there’s a fixed cosmic event horizon, ~62×109 light-years away
  Objects beyond it are inaccessible to us!
Where our SLC is today
46.6 Gly
62 Gly
Our cosmic causal horizon
13.4 Gly
Our observed SLC (CMB)
Local supercluster

## Slide 42: Brownian vs. Ballistic Reversible Machines
Bennett’s early examples of reversible computing mechanisms were primarily of the Brownian type
  Made forward progress only slowly, via a random walk
  Energy input could bias walk in a desired direction
    But, progress would still be slow and non-uniform
Fredkin and Toffoli at MIT wanted to find reversible logic mechanisms that were ballistic
  I.e., signaling mechanisms should make continual forward progress through the computation at a steady rate by “coasting” under their own momentum,
    with little energy lost per operation
This led to the conceptual Billiard Ball Model of physical reversible computation…