## Slide 1
J. Jacobson May 10, 2006
Center for Bits and Atoms Energy and Computation Workshop
Massachusetts Institute of Technology
Quantum Fusion
14.1 MeV

## Slide 2: Hot Fusion
The deuterium-tritium fusion reaction rate vs. temperature
Characteristic Fusion Energy / Chemical Energy
= 17.6 MeV / 13.6 eV ~ 106
Electrostatic Energy Barrier ~ 0.1 MeV (kT ~1 G Kelvin)
Effective Fusion at 10 KeV (108 Kelvin) – Botlzman Tail,
Tunneling
Hot Fusion: Beam – Target,Beam-Beam,Magnetic Confinement (‘Tokomak’), Electrostatic Confinement (‘Fusor’),Thermo-nuclear
www.wikipedia.com
Triple Product:
2D+2D | 3.27 MeV | 5.2E-13 Joules
2D in seawater | 30 g/m3 | 9.03E+24 atoms
Energy/m3 | 2.4E+12 Joules | 6.6E+08 W-H
Total U.S. Annual Energy Consumption | 3.6E+15 Watt Hours | 
Volume of Sea Water Required | 5.5E+06 m3 | 
Total Energy in World Ocean | 8.5E+26 Watt-Hours | 
Years of U.S Consumption | 2.4E+11 Years | 
Gallons of sea water needed for each gallon of gasoline | .014 Gallons | 

## Slide 3
(1) | D | + | T | → |  | 4He | (3.5 MeV) | + |  | n | (14.1 MeV) |  |  |  |  | 
(2i) | D | + | D | → |  | T | (1.01 MeV) | + |  | p | (3.02 MeV) |  |  |  |  | 50%
(2ii) |  |  |  | → |  | 3He | (0.82 MeV) | + |  | n | (2.45 MeV) |  |  |  |  | 50%
(3) | D | + | 3He | → |  | 4He | (3.6 MeV) | + |  | p | (14.7 MeV) |  |  |  |  | 
(4) | T | + | T | → |  | 4He |  | + | 2 | n | + 11.3 MeV |  |  |  |  | 
(5) | 3He | + | 3He | → |  | 4He |  | + | 2 | p | + 12.9 MeV |  |  |  |  | 
(6i) | 3He | + | T | → |  | 4He |  | + |  | p |  | + | n | + 12.1 MeV |  | 51%
(6ii) |  |  |  | → |  | 4He | (4.8 MeV) | + |  | D | (9.5 MeV) |  |  |  |  | 43%
(6iii) |  |  |  | → |  | 4He | (0.5 MeV) | + |  | n | (1.9 MeV) | + | p | (11.9 MeV) |  | 6%
(7) | D | + | 6Li | → | 2 | 4He | + 22.4 MeV |  |  |  |  |  |  |  |  | 
(8) | p | + | 6Li | → |  | 4He | (1.7 MeV) | + |  | 3He | (2.3 MeV) |  |  |  |  | 
(9) | 3He | + | 6Li | → | 2 | 4He |  | + |  | p | + 16.9 MeV |  |  |  |  | 
(10) | p | + | 11B | → | 3 | 4He | + 8.7 MeV |  |  |  |  |  |  |  |  | 
Fusion Reactions with Largest Cross Sections
fuel | T[KeV] | <σv>/T² [m³/s/keV²]
D-T | 13.6 | 1.24×10-24
D-D | 15 | 1.28×10-26
D-3He | 58 | 2.24×10-26
p-6Li | 66 | 1.46×10-27
p-11B | 123 | 3.01×10-27
Cross Sections

## Slide 4: Hot Fusion-ITER
Performance and Testing Requirements
Achieve inductive plasma burn with power amplification, Q (ratio of fusion power to auxiliary heating power), of at least 10 short term, steady-state operation with Q > 5;
Design Requirements
Engineering choices and design solutions make maximum use of existing R&D.
Average neutron flux > 0.5 MW/m2
Average fluence > 0.3 MWa/m2
Later installation of tritium breeding blanket should not be precluded.
Operation Requirements
The device is anticipated to operate for ~ 20 years, using externally supplied tritium.
Operational: 2016
Fusion Power Output: 500 MW (500 S)
Fuel Load: 0.1g D,T
Cost: 9 years * $360 M per year ~ $3.24 B
(Fission reactor ~ $4 B for 1GW ).
ITER Technical Obectives

## Slide 5: Hot Fusion-Pyroelectric Crystal Fusion
“Observation of nuclear fusion driven by a pyroelectric crystal”
B. Naranjo, J.K. Gimzewski and S. Putterman
Nature 434, 1115-1117 (28 April 2005)
820-keV 3He (lower panel) and a 2.45-MeV neutron (upper panel)
D + D -> 3He (820 keV) + n (2.45 MeV)
Lithium tantalate (LiTaO3)
pyroelectric crystal 120 KV
25 V/nm
103 Neutrons /s
10-8 Joules per 5 minute heating cycle

## Slide 6
http://www.brian-mcdermott.com/fusion_is_easy.htm
Jon Rosenstiel's Fusor: This fusor currently holds the amateur record with a fusion output of 107 ( "ten to the seven" or "10 million") fusions per second
"Fusion is Easy!"
The Homemade Amateur Nuclear Fusion Reactor
Farnsworth Fusor
Efficiency:
10-2 to 10-4 breakeven
Record: 1010 neutrons/sec
4000 Watt input

## Slide 7:  Catalyzed Fusion
L.W. Alvarez, H. Bradner, F.S. Crawford Jr., J.A. Crawford, P. Falk-Vairant, M.L.
Good, J.D. Gow, A.H. Rosenfeld, F.T. Solmitz, M.L. Stevenson, H.K. Ticho and
R.D. Tripp, Phys. Rev., 105 (1957) 1127.
F.C. Frank, Nature, 160 (1947) 525.



e

## Slide 8: Photonic De Broiglie Waves
“Photonic De Broglie Waves,”
Jacobson, Bjork, Chuang, Yamamoto PRL 74,4835 (1995)
I
I
I
I
I2
2I
“De Broglie wavelength of a non-local four-photon state,” P. Walther, J.W. Pan, M. Aspelmeyer, R. Ursin, S. Gasparoni and A. Zeilinger, Nature 429, 158 (2004)

## Slide 9
Beam-Target Fusion Using Quantum Measurement
Energy barrier ~ 0.1 MeV
Problem with Beam-Target Fusion is:
Cross section: ~ 10-24 m
r=r0 A1/3~ 1.3*10-15
Question: How much energy is required to target incident 2D to
Nuclear radius (~1 fm)?
 ~ 1/Sqrt [N] standard quantum limit and 1/N in Heisenberg limit.
10eV photon ( = 124 nm)
We need ~ 108 photons = 109 eV to localize D2 to 1.24 fm
Nuclear radius. Total energy extracted is: 3.3x106 eV
Require Cluster of 300 atoms

## Slide 10
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
p,n
e-
|N>
 ~ 1/ [N] Heisenberg Limit
Beam-Target Fusion Using Quantum Measurement