## Slide 1: Low-Power Statistical Computing with Analog Logic
Ben Vigoda
Advanced Technology Office (ATO) (BAA 04-09)

## Slide 2: Energy

## Slide 3: Ubiquitous Networked Computation

## Slide 4: The Problem

## Slide 5: Our Solution: Analog Logic
Combine Efficiency of Analog Device Physics
  >10x Less Power
  10x Less Area / Cost
  Unlike Digital, Can Operate in SiGe or GaAs
With Scalability of Digital Signal Processing
  Modular, Hierarchical for Automated Design Synthesis
  Invariant to Fabrication Process
  Currently Designing Analog Logic IC’s with Computational Complexity Equivalent to Millions of Digital Devices
  Programmable

## Slide 6: Analog Logic for Wireless Communications
Complex Signal Processing Algorithms in “Analog” Electronics
  Replace Baseband DSP
  Augment RF Capabilities
  Smooth “Adiabatic” Conversion from Uncertainty to Certainty

## Slide 7: Belief Propagation on Factor Graphs includes a very wide range of signal processing and machine learning algorithms
Filtering and Control

## Slide 8: From Logic Gates to Analog Logic Gates
x | y
0 | 1
1 | 0
Instead of a zero,
we have an 80% chance of a zero
And btw, p(0) + p(1) = 100%

## Slide 9: Factor Graph Example: probability inverter
x | y
0 | 1
1 | 0

## Slide 10: Factor Graph Example: probability inverter
x | y
0 | 1
1 | 0

## Slide 11: Factor Graph Example: probability XOR
X | Y | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 12: Factor Graph Example: probability XOR
X | Y | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 13: Factor Graph Example: Error Correction Encoding

## Slide 14: Factor Graph Example: Error Correction Decoding

## Slide 15: Soft-Gates In General
Factor Graphs and the Sum-Product Algorithm. Kschischang, Frey and Loeliger. IEEE Transactions on Information Theory, 1998.
Notes: In the last slide I kind of waved my hands to write down the soft-xor function
But essentially the soft-xor is saying that p(z) = p(y)p(z) but subject to the mod 2 constraint
And so if we have another kind of logical constraint, we can derive a soft-gate for it.

## Slide 16: Factor Graphs: Joint Marginals (Generalized Belief Propagation)
Constructing Free Energy Approximations and Generalized Belief Propagation Algorithms. Yedidia, Freeman and Weiss. IEEE Transactions on Information Theory. 2002

## Slide 17: Fourier Transform of a Factor Graph
Codes on graphs: Normal realizations. Dave Forney

## Slide 18: Analog Logic Circuit: “Soft-XOR” Circuit
Digital CMOS Circuit:
XOR Gate
Notes: bits in coding (0,1) suggests a dual rail circuit representation of p(0), p(1) in currents, log-likelihood in voltage

## Slide 19: Analog Logic Gates
TSMC .18um digital process (1.8V supply)
1 Analog Logic gate is equivalent to > 103 digital gates
Up to ~1GHz Bandwidth (~1mA per AL gate)
Notes: Actual values from simulation - SNR in circuits, power consumption, speed, etc.
Verify 1uW with Yael.
For soft decoding we want about 5-8 bits of resolution - around 100 discretely recognizable analog levels.
The dynamic range plus the SNR put a bound on this. Get from thesis argument.

## Slide 20: Transfer Function of 2-Input SoftXOR Analog Logic Gate
Theory
Measurements

## Slide 21: Analog Logic Modular Workflow
Simulate factor graph algorithms in JmpLab (Java message passing Laboratory).
Notes: Actual values from simulation - SNR in circuits, power consumption, speed, etc.
Verify 1uW with Yael.
For soft decoding we want about 5-8 bits of resolution - around 100 discretely recognizable analog levels.
The dynamic range plus the SNR put a bound on this. Get from thesis argument.

## Slide 22: Analog Logic Modular Workflow
Find minimum realization of factor graph. (Similar to RTL synthesis)
Notes: Actual values from simulation - SNR in circuits, power consumption, speed, etc.
Verify 1uW with Yael.
For soft decoding we want about 5-8 bits of resolution - around 100 discretely recognizable analog levels.
The dynamic range plus the SNR put a bound on this. Get from thesis argument.

## Slide 23: Analog Logic Modular Workflow
Compile factor graph into circuit schematic and simulate in Cadence circuit simulator.

## Slide 24: Analog Logic Modular Workflow
Cadence software to design and re-simulate our layout
Essentially thousands of “mixer” circuits on one substrate

## Slide 25: Analog Logic Enables Complex Signal Processing in RF Front-ends
Complex Signal Processing in “Analog” Circuits
  Adaptive Filtering
  Signal Selective Gain
  Interference Rejection
  Arbitrary Waveform Generation and Selection
No DAC, No ADC
Frequencies and bandwidths that would be heroic in digital
Can Implement in High-Speed Process (SiGe)
100x Less Power

## Slide 26: Noise Lock Loop (NLL) Circuit
Noise Lock Loop:
  Tx: Generate arbitrary wideband waveforms
  Rx: Amplify a family of wide-band waveforms, while rejecting interference
Applications in UWB, Radar, and GPS
Synchronization of Pseudo-Random Signals by Forward-Only Message Passing with Application to Electronic Circuits. IEEE Transactions on Information Theory, August 2006. Vigoda et al.

## Slide 27: Comparison of Noise Lock Loops Built Using Analog Logic vs. Digital ASIC
 | Analog Logic | Digital Logic
Power | ~200uW | ~20mW
Number of Transistors | ~150 analog transistors | ~6000 digital transistors

## Slide 28: Analog Logic Replaces Baseband DSP
Baseband Algorithms Implemented in “Analog” Hardware
  LDPC / Turbo Decoding
  MIMO Estimation and Decoding
  FFT / Spectral Estimation
  Demodulation / Channel Equalization
  Filtering / Interpolation / Prediction
Eliminate Analog-to-Digital Converter
  Exponential Power/Cost Savings
Comparison to Baseband Digital ASIC
  10x Less Silicon Area / Cost
  10x Less Power + Savings From Eliminating ADC

## Slide 29: Analog Logic Low-Power, Low-Latency Low Density Parity Check (LDPC) Decoder
Just 3 man-months to produce analog circuit with 30,000 analog transistors
Designed for WiFi/WiMax
No ADC necessary

## Slide 30: Comparison of LDPC Decoders We Are Building Using Analog Logic vs. Digital
 | Analog Logic | Digital Logic
Power | ~75mW | ~750W
Area | 2 mm2 | 20 mm2
Design Time | 3 person-months to schematic | 3 person-months to VHDL
Number of Transistors | 30,000 analog transistors | Several millions digital transistors

## Slide 31: “Adiabatic” Radio Receiver Using Analog Logic

## Slide 32: Partners
Advanced Technology Office (ATO)
Analog Logic Seedling (BAA 04-09)
OpenChoice Program
MIT Analog and Biological Systems Group
Professor Rahul Sarpeshkar
MIT Media Lab, Center for Bits and Atoms
Professor Neil Gershenfeld, Director

## Slide 33: Factor Graph Example: Marginalization on Tree (message passing metaphor)
Notes: Now let’s combine a couple of different kinds of factor nodes – “soft-gates”

## Slide 34: Design Tool Assisted Optimization of Circuits Is Essential
Digital design would be impossible without software to help automatically optimize the design and layout of logic.
To make optimization of analog circuits tractable, use small library of modular primitives.