## Slide 1: Fablab: Thinner Client
Peter A. Bosscha
June 2006

## Slide 2: Agenda
Background
Current Status
Future Ideas

## Slide 3: Background The Idea
Bringing computing / messaging to community
One Model:
  Fablab has Internet access and real computing power.
  Community around the Fablab benefits by networked connections to the Lab, using Fablab technology to build their computing & networking needs.
In ICT world this is known as Thin Clients

## Slide 4: Background Thinking
What are the needs:
  Messaging
  Document creation & printing (CV)
  Browsing (Data Access)
What is available already in terms of input, output and communication devices.
  Mobile Phones
    Problem: Diverse models
  TV as a display

## Slide 5: Current Status Overview

## Slide 6: Current Status VNC
Open protocol
Server has screen content and performs all computing.
Client requests screen updates
Connection is state-less. (Travel around the world to another computer, pick up where you left off.)
Experiments: SLIP interface 115KBaud 320x240 is workable.

## Slide 7: Current Status First Iteration
VNC is do-able but might not fully meet our needs.
Text based computing for a first iteration. (Less bandwidth)
Decided on VT-100 Terminal, serial interface.
Possible applications:
  Text Based Browsing (Lynx)
  Text Based E-Mail (Mutt)
  Document editing (Nano, VI)

## Slide 8: Current Status Video Part
Revision 1:
  Mega16 (IO) + SRAM
  PAL Output
  Capable of 320 * 240 Grey Scale
  Serial Interface, 230KBaud
Revision 2:
  Character Generator
  VT-100 Emulation
  Serial Interface now 9600Baud
  Code Size: +/- 4KByte
Cost: +/- 5 USD

## Slide 9: Current Status Keyboard
Interfaces to standard PC-Keyboard (US)
Serial Output

## Slide 10: Current Status Demo Idea

## Slide 11: Current Status Economics
Hardware is flexible, does not have to be TV, could be small LCD’s.
Hardware is low cost, +/-20 USD for working implementation.
Businesses might grow from this;
  network maintenance
  terminal manufacture and customisation

## Slide 12: Future Ideas
Keyboard to be done using Fablab technology
Add I0 Radio link, work out bandwidth requirements.
Use Wavelet encoding for true graphic interface.
Pointing Device from Fablab technology.
  Tilt Sensor