## Slide 1: Internet 0 @ Schneider Electric Todd A. Snide, 12 October 2006
Automation Business Unit
Notes: 1

## Slide 2: The Internet 0 Value Proposition
IP at all Levels
  Current models require different protocols and translation to communicate
  The SE model uses IP communications at all levels; no translation.
Cost Effective for Simple Devices
  By using the power lines for communication, Internet 0 has a lower port cost and installation cost.
  The potential total cost for components can be < 1 €
  There are no cabling costs
€
The Competitor’s Model
The Schneider Electric Model
< €

## Slide 3: Potential I0 Applications for Schneider Electric
Industrial Automation
  The first target devices are simple items such as push buttons, pilot lights, relays, thermometers, etc.
  Devices that do not change state often and can support a low data rate (1 megabit per second).
  The first Schneider Electric version of Internet 0 Devices are 24 Volt DC based.
Building Automation
  Lighting, HVAC applications, sensory, energy savings
Electrical Distribution
  MCC panel network
As the Internet 0 network is proven reliable, higher-end devices can be supported.
Push Buttons
Pilot Lights
Relays

## Slide 4: Why this demonstration?
To address three key questions about the technology
  Will it work in Schneider product applications?
  What are the technical capabilities and limitations?
  Are the per node costs as advertised?
We chose the Schneider Electric All in one panel architecture to help validate the Internet 0 technology
  It is a fully contained network usually with a communication path to a control network which closely matches our prototyping model.
  It has sufficient number of devices using 24 volts DC where most of the communication will be local to the panel.
  Each panel has a different function which will prove out our networking model for Internet 0
All in one panel
Safety
Power
supply
Motion
I/O
Controller
Motor
starter
Drive
HMI
I/O
I/O

## Slide 5: Project Status
A network of 25 Internet 0 nodes has been developed using simple Industrial Automation devices.
  Pilot-lights, push-buttons and push-button/pilot lights.
A simple Internet 0 SLIP bridge is used to interface to a computer.
The network operates at 24 volts DC.
The network works at its original speed with no speed improvements added at this time. (about 400 kilobits per second)
The maximum distance for communication between 2 nodes to date has been 31 meters.
  The signal was degraded but the true distance limit of communication has not been determined but is certainly longer than 30 meters.
The only connection to the node and device combination is the two wire power lines.

## Slide 6: Opportunities:
Performance characterizations
  More randomized traffic from several nodes
  Perform 4-corner testing; max # of nodes, max. distance, max daisy-chain
  Include some “noisy” devices in the network
Performance improvements (without added cost)
  Currently the bit width, time between bytes and time between packets is fixed and very long, shorten the time between the bytes and packets
  Enhance the collision detection
  Allow packets to be interleaved during transmission
  Optimize the current code
  Increase the internal operating speed of the processor
Performance improvements (increased cost)
  Run the processor at 20MHz using and external crystal and capacitors
A trade-off between network speed and node cost will need to be characterized

## Slide 7: Conclusions
Summary
  Internet 0 is viable for simple devices in All-In-One-Panel applications
    Networking simple devices is truly viable
    The reduction of the per node cost is significant.
    The visibility a network administrator can have with Internet 0 is greatly enhanced.
  It is worth exploring the use of Internet 0 in higher performance devices and Human Machine Interface-like devices
  We believe other Schneider Electric business units could use Internet 0 in other physical mediums