## Slide 1: Fabricational Capacity
MAS 960 collective:
N. Gershenfeld, J. Jacobson, S. Kirkpatrick, L. Lafuente, Y. Maguire, B. Vigoda, D. Dalrymple, G. Popescu, K. Chuang, M. Baca, A. Sphunt, A. Knaian
Notes: In this morning session, we have been witness of the dramatic progress that is going on fabrication technology, from fabricating with DNA to fabricating at the scales of entire buildings. Now it’s time to ask where might this amazing progress lead and where it can not, where are the limits of fabrication?

## Slide 2: Foundations
Notes: Let’s start by establishing a historical parallelism between this situation and the one given when digital communication and digital computation emerged.

## Slide 3: Shannon on Digital Communication
Rate
Error
After Shannon
Before Shannon
Non Achievable
Achievable
Encoder
Decoder
Noisy
Channel
Source
Channel capacity
Notes: When Shannon arrived at the Bell Telephone Company, the engineers were dealing with the problem of reliable communication through unreliable or noisy channels. The sound waves in the telephone were transformed to electrical waves which were transmitted through telephone wires and they were corrupted by electrical noise and cross-talk with other lines. Shannon was the first in analysing separately the message from the channel. Adding some redundancy to the message would allow to recover it, even if it was modified by noise. The more noise, the more redundancy you need and the lower rate you can communicate. At that time, there was a widespread belief that in order to achieve a vanishingly small error probability, one would have to reduce the rate correspondingly close to zero. That’s the meaning of blue and green curves.
Shannon, by digitazing the message, was able to prove both that reliable communication at any rate beyond a threshold is impossible, and that reliable communication at all rates up to the theshold is possible that’s red curve in the figure). This threshold is called channel capacity and it depends upon the characteristics of the channel (for a Gaussian channel, the bandwidth and the signal-to-noise ratio).

## Slide 4: Von Neumann on Digital Computation
ENIAC
Shannon’s theory applied to digital computation
Reliable computation using unreliable components
m
m
m
m
u
Notes: For digital computation we should start with the first general-purposed programmable digital electronic computer, the ENIAC. One of the major drawbacks of the ENIAC was unreliability. Each time a vacuum tube crashed, and that happen almost once per day, it had to be replaced in order to obtain reliable computations. That led Von Neumann to apply Shannon’s theory of communication to show how to compute reliably with unreliable parts. He studied logical circuits which perform the computation redundantly and then remove the mistakes, producing a perfect result. Like Shanon, he was able to show that for these systems there exist thresholds, such that if the probability of error in the components is not too large (and the meaning of that depends on the characterstics of the system) you can still obtain the exact answer.

## Slide 5: Von Neumann on Self-Reproducing Automata
Notes: After the ENIAC and thanks to Von Neumann work, more and more complex machines appeared in scene. That led Von Neumann to study the limits of engineering and also life organisms as the limit of high or extremely high complicated systems. Due to the technical limitations of those days, Von Neumann created for his purposes a virtual world of cellular automata (discrete mathematical models of machines), with the abilty of self-reproduction. In the figure we can see how the automata load the construction design in the memoty unit and builds a copy of it by the construction unit. Nowadays, this abstract world has been materialize in silicon and it’s the matter of very serious research.

## Slide 6
Notes: Given this, we think it’s mandatory to ask for the same questions for fabrication as Shannon and Von Neumann did creating complete new fields of research which involved a dramatic technical and social impact.

## Slide 7: The Problem

## Slide 8
Process
Final Product
Raw Material
Space
Time
Power
Resources
Notes: Given a process which transforms raw material into a desired state, independent of the process, is there a way to assess limits on how well it can be done that let you evaluate good ways versus bad ways to do it?

## Slide 9
Trade-offs
Thresholds:
  Feasibility
  Efficiency of the implementation

## Slide 10: Towards a Solution

## Slide 11: A quantitative proposal
Second Law of Thermodynamics:
Thermodynamics-based metric:
Notes: Our proposal to fabricational capacity is driven by thermodynamics. Consider a finite classical system in contact with a heat reservoir. A central concept in thermodynamics is that of the work performed on such system, when some external parameters are change in time (in a broad sense that’s what you do in a fabrication process). When you do that infinitely slowly from initial state A to final state B, then the work is equal to the Helmoltz free energy difference. But when the parameters are modified at a finite rate, then the work will depend on the microscopic initial conditions of state A and will, on average, exceed delta F. Therefore, delta F is the minimum amount of work needed to go from state A to state B. Given the raw material and the final product, you could evaluate the efficiency, in terms of this metric, using that quantity.

## Slide 12: Some working examples
Freezing (Crystal manufacturing)

## Slide 13: Some working examples
Master DVD production

## Slide 14: Some working examples
Car manufacturing (River Rouge plant)

## Slide 15: Some working examples
C. Elegans

## Slide 16: A CA approach
Space
Time
Transition probabilities
Uncertainty models unreliability
Maps to effective equilibrium Statistical Mechanics models