## Slide 1: Internet 0 for Industrial Applications
Fred Cohn 13-Dec-07
Notes: <number>
<footer>
<header>
<date/time>
1

## Slide 2: Example Applications in Industrial Automation
Internet 0 is most like AS Interface for Industrial Automation networks and could be located on the same level of devices
  Like AS Interface, Internet 0 devices would send their signals over the 24 volt supply lines.
  The same form of signal modulation could be used.
  Both protocols use Manchester II encoding.
An All-In-One-Panel applications are ideal.
  Each cluster of Internet 0 devices would have their own IP Address sub-net.
  Each sub-net would be connected to the controller through an Ethernet bridge. Connections between the sub-nets would also be over Ethernet.
  Replace hard wired (I/O circuits) for best cost reduction

## Slide 3: Typical Manufacturing Cell
Complex Machine
Compact Machine
Simple Machine
On site
Maintenance
Cell Monitoring
and Control
Back-Up
Maintenance
Quality
ERP
MES
Router/Firewall
Global Monitoring
and Control
(Plant Level)
Ethernet
(Cell Level)
Ethernet
Firewall
Intranet/
Internet
Remote
Monitoring
and Control
Ethernet
Smart device
Transparent Ready Solution Approach – Manufacturing example
Ethernet
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: System Architecture – Factory Automation – Solution Approach
Information & Control
Fieldbus
Machine Bus
Sensor Bus
Multi-Tiered Strategy
Ethernet TCP/IP for Information, Control and Fieldbus
CANopen for Machine Bus
SERCOS for Motion Bus
AS Interface for Sensor Bus and Safety
Ethernet TCP/IP Protocol
Today, Modbus TCP
Future, EtherNet/IP and Modbus TCP converged into a single solution
Motion Bus
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: All-in-One Panel - Preferred Implementations 1/2
Hardwired cabling
1
Internet 0 to Replace
Hardwired cabling:
Reduce install costs
Eliminate I/O circuits
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: All-in-One Panel - Preferred Implementations 2/2
Internet 0 to Replace
ASi Interface:
Improve performance
Reduced wiring cost
1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Requirements for Low End Fieldbus
Low cost:
  Lower cost, per node than Ethernet, CANopen, or ASi Interface
  Low cost of cabling
  Assuming we start with 24VDC for control signals
Easy to Use
  Installable and Configurable by maintenance electricians; minimal tools and addressing complexity
Easy to Diagnose and Maintain
  Problems diagnosed and products replaced by maintenance electricians
  Small web server for each device is a very interesting architecture
Acceptable Performance
  Targeting simple devices normally depending on human intervention; PBs, PLs
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Advantages of Internet 0
Internet 0 brings IP connectivity and continuity down to the lowest level in the automation network.
Communication to all levels in the total network is transparent to the user. No protocol translations are needed.
Port cost is very low.
Installation cost and complexity is reduced since the 24 volt supply lines are also used as the communication lines.
  There is no additional cost of a second communication line.
  The installation technician requires no extra knowledge or tools.
Enhanced services are available to the user like small web pages.

## Slide 9: Disadvantages with Internet 0
Internet 0 is not an accepted standard at this time.
The written standard for the stack has not been fully developed.
Internet 0 uses a UDP based stack, Modbus over UDP needs to be understood.
Configuration of Internet 0 devices needs to be defined.
  Use of DHCP and BootP may need to be included in the stack.
  Use of Schneider signature rotary switches may need to be adapted.
Use of Internet 0 over AC lines has not been developed.

## Slide 10: Existing Advantys Demo
The STB Drives Demo is essentially an All-In-One-Panel in a suitcase.
Advantys STB Ethernet-based I/O System
Magelis HMI 2 line display
ATV31 Variable Speed Drive
Tesys U Motor Starter
AC Motor
Push buttons, pilot lights, potentiometer and analog display

## Slide 11: Initial location of the Internet 0 nodes (ports)
Only the simple devices will use Internet 0 to replace hard-wiring.
The motor starter and potentiometer will be investigated
Push buttons
Pilot lights

## Slide 12: Internet 0 Productization Concept
Advantys will have direct control and access to the Internet 0 network.
An Advantys module might be needed to make this possible.
A similar module could be designed for any other control platform or PLC.
The Internet 0 device web pages can be brought out to an external computer for display.
Computer to display any selected communications.
Ethernet
cable
Advantys module interfacing directly to the Internet 0 network.

## Slide 13
Thank You