## Slide 1
Coming soon… The Internet of Things
Mathilde Durvy - mdurvy@cisco.com
Corporate Development Technology Group

## Slide 2: Why IP for Wireless Sensor Networks?
Standardized and open protocol
Interoperability
  between different sensor networks
  with existing IP networks
Link-layer agnostic
Reuse established protocols running in the Internet
  Transport protocols
  Easy management and troubleshooting
  End-to-end security
  etc
Notes: - Link-layer agnostic, 802.15.4, WiFi, PowerLine, etc
- Reuse existing protocols such as UDP/TCP for transport, SNMP, traceroute, IPSec, Http, Html, XML, SOAP

## Slide 3: Two Key Steps to Establish IP as the Protocol for Wireless Sensors
IPSO
  The IP for Smart Object alliance
  Marketing effort
Contiki - μIPv6
  Joint project between Cisco, SICS, and Atmel
  The smallest, open-source, IPv6 Ready stack
Notes: IPSO launched in september this year, uIPv6 released mid-October

## Slide 4
Objectives of IPSO
Create awareness of IP technology for Smart Objects
Generate tutorials, white papers and use cases
Support the IETF
Combine / coordinate member marketing efforts
Organize interoperability events
Notes: IETF: Routing Over Low power and Lossy Link (ROLL) WG, IPv6 over Low power WPAN (6LoWPAN)

## Slide 5: The IPSO Alliance Members
EDF R&D
Kinney Consulting
PicosNet
ROAM
www.ipso-alliance.org
Notes: 27 funding members
companies that specialize on senor networks: nivis, arch rock, dust, sensinode
Chip manufacturers: Atmel, freescale
Large companies: SAP, SUN, Cisco, ericson
End-users like Duke energy or EDF
Academic partners

## Slide 6: The μIPv6 Stack – Overview
Open-source
  Released in October, now part of Contiki 2.2.2
  Available for commercial and non-commercial use
Small footprint
  Code size ≈ 11.5 KB
  RAM usage ≈ 0.2+1.6 =1.8KB
  Fit on the most constrained platforms
Certified
  IPv6 Ready Phase-1 Logo
  - Interoperable with stacks of all main vendors
3 addresses, 3 prefixes, 4 neighbors, 2 routers + a 1280 packet buffer
Notes: \postersection{IPv6 Ready Logo Program}
\item The only certification authority for IPv6
\item Tests conformance to standard and interoperability
\item Devices from all major vendors have the IPv6 Ready Logo
\item $\mu$IPv6 is the first stack for sensor nodes to obtain the IPv6 Ready Phase-1 Logo
\item More information at http://www.ipv6ready.org/
%----
\postersection{Open-source}
\item BSD-like license
\item Available for commercial and non-commercial use
\item $\mu$IPv6 is part of the Contiki operating system
(http://www.sics.se/contiki/)
\item Active mailing-lists and numerous developpers
\item KAME stack comes from JAPAN, now used in NetBSD, FreeBSD
%----
\postersection{Small footprint}
\item $\mu$IPv6 can fit on the most constrained platform
\item The code takes $\simeq$ 11.5 KB of ROM
\item The data structures use $\simeq$ 0.5 KB of RAM
\item The single IP packet buffer $\simeq$ 1.3 KB of RAM
\item Possible additions (decided at compile time)
\item IP fragmentation (+ 1.3 KB)
\item Per neighbor buffering during address resolution (+ 1.3 KB per neighbor)

## Slide 7: The μIPv6 – Design
IPv6 Specification (RFC2460), and IPv6 Addressing Architecture (RFC4291)
Neighbor Discovery (RFC 4861)
Stateless Address Autoconfiguration (RFC4862)
ICMPv6 (RFC4443)
μIPv6
Notes: \item $\mu$IPv6 runs as a Contiki protothread and is tightly coupled to Contiki's UDP and TCP protocol implementations
\item $\mu$IPv6 does not assume a specific link-layer (it was tested on Ethernet and 802.15.4+6lowpan)
\item $\mu$IPv6 implements the following main standards:
\item RFC2460, IPv6 Specification (packet, header, options format)
\item RFC4291, IPv6 Addressing Architecture (addressing model, representations of IPv6 addresses, definition of IPv6 unicast addresses, anycast addresses, and multicast addresses, and an IPv6 node's required addresses)
\item RFC4861, Neighbor Discovery (discover each other's presence, to determine each other's link-layer addresses, to find routers, and to maintain reachability information about the paths to active neighbors)
\item RFC4443, ICMPv6 (Internet Control Message Protocol: ping, error messages)
\item RFC4862, Stateless Address Autoconfiguration (generating a link-local address, generating global addresses via stateless address autoconfiguration, and the Duplicate Address Detection procedure to verify the uniqueness of the addresses on a link)

## Slide 8: Feedback to IETF
Fragmentation
Per neighbor buffering
Avoid large packets – ICMP errors
Neighbor cache updates
Options and extension headers processing
space
space
power
complexity
Notes: MAJOR (RFC 4861): The requirement to keep one packet per neighbor during address resolution implies (nb neighbors)*1280 bytes buffers.
MINOR (RFC 2460): The fragmentation of large packets (above 1280 bytes) would require a 1500 bytes buffer.
MAJOR: Avoid big packets when the link-layer is resource limited. For example in ICMP error (RFC 4443), include faulty packet only up to the L2 MTU (127 for 802.15.4), and not up to L3 MTU (1280 for IPv6).
Complexity of NS/NA processing (though it should be replaced with white board)
Complexity of options and extension headers processing: Be liberal in what you accept, and conservative in what you send

## Slide 9: The Platform – Atmel’s AVR RAVEN
AT86RF230
  2.4GHz transceiver
ATmega1284P
  Communication stack
  128KB Flash, 16KByte SRAM
ATmega3290P
  User interface
  Audio
Notes: Two AVR 8bit RISC microcontrollers
Audio = speaker (big circle) + microphone (upper right corner of speaker)
User Interface = LCD screen + Audio
Sensors= NTC temperature (bottom right corner)

## Slide 10: Sensys 2008 Best Poster Award
MAC 02:11:11:ff:fe:11:11:11
Link-local IPv6 fe80::11:11ff:fe11:1111
Global IPv6 aaaa::11:11ff:fe11:1111
Default Router
Advertizes prefix aaaa::/64

## Slide 11: Summary
The Internet of Things is happening
Marketing tool = IPSO
IP to the sensors = μIPv6